## Slide 1: Periodic Maintenance Service (PMS) Project
18 August 2026
ISUZU TRUCK UK LTD

## Slide 2: Contents
Maintenance Interval Implications
PMS Project Outline
ISZJ PMS Requests & ITUK Response
Promotion Parts List – BVP Queries
Parts \ Service Flow
Connected Pathway
Maintenance Package Pathway
KPI Proposal
Implementation Roadmap
PMS Part Numbers By Model
Support

## Slide 3: Maintenance Interval Implications
Segment
Model / engine
Interval basis
Campaign implication
N35.125
NLR87 / RZ4E
20,000 km
Secondary service-reminder campaign only
N35.150
NLR88 / 4JZ1
Flexible up to 40,000 km
Secondary, where customer data is reliable
N75
NPR75 / 4HK1
40,000 km
Phase 1 target - fleet, R&M and safety events
N75
NPR88 / 4JZ1
40,000 km
Phase 1 target - fleet, R&M and safety events
Do not use old NLR85 / 4JJ1 assumptions as the basis for the launch plan.

## Slide 4: PMS Project Outline - Protect Uptime and TCO
Our proposal translates the ISZJ PMS objectives into a UK-ready operating model that can be launched from October.
1
Target the reachable opportunity
Start with N75 fleet / R&M / safety-event customers where workshops already have repeated touchpoints. Followed by N35 customers currently not using the network.
2
Sell the right items first
Air Filter and Brake are the headline items; Oil and Fuel are the 40,000 km PMS pack foundation.
3
Standardise dealer execution
Use PMS Standards: Service Advisor proposal, Technician check sheet and Parts Stock.
4
Move to connected triggers
Use odometer + geofence + history to create due-work reminders and feed maintenance packages for future models.
1
Identify N75 fleet events
Use R&M, service-contract and dealer safety-inspection schedules.
2
Pre-check VIN / engine / mileage
Confirm NPR75 or NPR88 and the correct 40,000 km pack.
3
Prepare PMS filter pack
Oil + Fuel + Air filters ready before the workshop visit.
4
Inspect brakes during safety event
Record pad condition and convert where replacement is needed.
5
Quote, convert or follow up
Capture declined work as the next PMS reminder opportunity.
Align PMS parts with the fleet safety-event cycle to protect uptime and avoid repeat workshop visits.

## Slide 5: Why the UK launch must be N75-led
7.5t operators are professional, compliance-led and highly sensitive to downtime and whole-life cost. The campaign must create uptime value, not just additional parts sales.
N75
7.5t fleet focus
Easier to identify through R&M, service contracts and safety inspections
40k km
Maintenance basis
NPR75 / 4HK1 and NPR88 / 4JZ1 campaign pack logic
6-8 wks
Safety events
Regular inspection cycle gives practical brake conversion trigger
TCO
Primary risk
Avoid pushing cost into loyal S1/S2 customers without value explanation
Service Interval Context
ISUZU N75 is more frequent than DAF, Mercedes/MAN and Iveco.
At 50,000 km/year, ISUZU is shown at approx. 1.25 services/year versus DAF at 0.5.
This makes PMS messaging more sensitive: we must position reliability and compliance benefits clearly.
Model Implication
Do not use old NLR85 / 4JJ1 assumptions as the launch basis.
N35 is Phase 2: use only where customer contact and mileage data are reliable.
N75 gives a measurable, event-led pilot with lower execution risk.

## Slide 6: Why the UK launch must be N75-led
The launch should not be a generic discount campaign. It should be a dealer workflow that attaches PMS parts to real N75 workshop events.
Headline
Air Filter
Low coverage / easy attach
Headline
Brake
Safety-critical conversion
Foundation
Oil + Fuel
Build the 40,000 km PMS pack
Controlled
Clutch
VIN-specific manual only
N75 fleet / R&M / Service-Contract / Safety-Inspection Records
October Launch Pilot
N35 becomes Phase 2: use service reminders only where customer contact and mileage data are reliable.

## Slide 7: Phase 2: PMS Target Customers – N35
NLR87 / RZ4E
N35.125 - 20,000 km basis. Use service reminders only where customer contact and mileage data are reliable.
NLR88 / 4JZ1
N35.150 - flexible interval up to 40,000 km. Use PMS pack offers for identifiable customers.
NLR85 / 4JJ1
Previous N35.120 model. Do not use as the calculation basis for the main launch campaign.
N35 message
"Do the full PMS filter set, not just the oil filter."
S1 (New Customer)
First time purchase for ISUZU Vehicles
S2 (Continuous Use of ISUZU Service Shop)
Customers have a clear intention to use ISUZU Service Shop
S3 (Non-continuous use of ISUZU Service Shop)
Customers are likely to use ISUZU Service Shop
S4 (No History to Use ISUZU Service Shop)
Customers clearly have no intention to use ISUZU Service Shop

## Slide 8: ISZJ PMS Requests & ITUK Response
Requirement
ITUK response
Output
Target volume scenario
Use practical 2025 ITUK Parts Sales + UIO data for targeting.
Baseline Coverage model
Finalise promotion programme for Oct launch
Phase 1 N75 campaign with dealer baseline, one-page guide (Bulletin) and monthly league table.
Implementation plan
Review parts list / BVP / low demand
Resolve 1876102860, 5876102500, 8983104491, 8983752250 and EU R90 brake pad action.
BVP action list
Discuss maintenance package / KPIs
Connect PMS to maintenance packages, contract rate, dealer events, genuine parts and fill-rate KPIs.
KPI’s
Use connected / odometer linkage
Odometer + geofence + history creates due-work trigger and S1-S4 classification.
Future Connected workflow

## Slide 9: Promotion Parts List – BVP Queries
Item
Issue
ITUK action
1876102860
BVP fuel filter: zero ITUK Parts Sales 2025
BVP alternative 8975425400
5876102500
BVP air filter: zero ITUK Parts Sales 2025
BVP alternative 8981772710
8983104491 / 8983752250
Low demand filters
S/S TO 8975425390
8982447940
EU R90 brake pad replacement for N75
Place initial order and add to R90-compliant brake pack after ISZE/ISZJ confirmation.
BVP availability, low-demand fuel items and the EU R90 brake pad.

## Slide 10: Parts \ Service Flow
Parts
Service Advisor
Technician
Inbound Parts Inspection & Put-away
Suggest Additional Items
Vehicle Handover
Vehicle Check-In & Confirm Authorised Work on Job Card
Dealer Inventory
Confirm Authorised Work & Mileage
Collect Required Parts
Perform Work
Fill Out Check Sheet & Job Card
Feedback to customer
Explain work completed & quote for additional work.
Hand Keys to Workshop Controller
Demand Forecasting & Orders
Issue Parts to Job card \ WIP
Interrupt Required Parts
Confirm Parts for Repair & Upsell Additional Items
Are all parts in stock?
Yes
No
Move Vehicle to Workshop

## Slide 11: Connected Pathway
The proposed approach can launch manually first, then strengthen as odometer linkage, geofence and DTC/DTU operations become available.
Vehicle data
Odometer
DTC/DTU
Location
Decision logic
Maintenance due?
S1-S4 customer type
Nearest dealer
Operational action
Contact Customer
Dealer quote
Pack pre-order
Commercial outcome
PMS conversion
Maintenance pack
Genuine parts retention
Core rule: Connected data to be used to reduce missed PMS events, reduce repeat visits and improve uptime.
Connected / Odometer Linkage: From static campaign to trigger-based PMS

## Slide 12: Maintenance Package Pathway
ISZJ asked how connected services, odometer linkage and packages can work together.
Connect
Warranty / roadside / connected
Maintenance reminders
I-Maintain record access
Essential
Safety inspections and compliance
Routine maintenance
Dedicated CARE executive
Value
Full R&M for chassis
Preventative Wear and tear
Tacho / MOT / contract management

## Slide 13: KPI Proposal
The project will fail if it is measured only as a parts discount activity.
The KPI set should track coverage, conversion, dealer capability and customer retention.
Commercial
PMS QTY / GBP
Cover ratio by category
Parts Sales Growth
Dealer conversion
N75 event conversion
Brake quote acceptance
Air-filter Increase Sales
Stock readiness
Fill rate
B/O items
Pack availability
Connected
Odometer due triggers
S1-S4 classification
CARE/dealer follow-up
Customer
Retention
Declined work recovery
Maintenance pack contract rate

## Slide 14: Implementation Roadmap
18 Aug
Japan alignment
Scope, Target, Support, KPI, BVP questions, and roles agreed.
Sep
Launch build
Dealer baselines & targets, part packs, stock rules, one-page guide
Oct 2026
Go-live
N75 Fleet Uptime PMS campaign launched
Nov-Dec
Pilot review
Conversion, availability, dealer performance and customer feedback
FY27
Scale decision
N35 expansion where data is reliable; maintenance package link
ITUK
Dealer execution, baselines, stock rules, service workflow, dashboard.
ISZE
Commercial support, incentive mechanism, BVP supply support.
ISZJ
PMS standard alignment, R90/BVP confirmation, connected requirements.

## Slide 15: PMS Parts Promotion – NPR75 N75 4HK1
PMS category | Part number | Description / note | Campaign priority | Monthly Average | Year To Date Demand | Comments
Oil Filter | 8983282071 | Element; oil filter | High | 5.2 | 47 | 
Oil Filter family | 8983282070 | Same HOF family / related oil filter reference | High | 41.8 | 371 | 
Oil Filter BVP | 1876102890 | BVP alternative for 8983282070 family | Useful for price-sensitive customers | 242.8 | 1,633 | 
Oil Filter BVP | 5876101170 | BVP alternative for 8983282070 family | Useful | 16.5 | 60 | S/S TO 1876102890
Oil Filter BVP | 5876100310 | BVP alternative for 8983282070 family | Useful | 0.0 | 0 | S/S TO 1876102890
Fuel Filter ASM | 8975425050 | Filter ASM; fuel | Medium-high | 2.6 | 15 | 
Fuel Filter Element | 8975425400 | Element; fuel filter | High | 289.3 | 2,065 | 
Fuel Filter BVP | 1876102860 | BVP alternative for 8975425400 | Useful | 0.0 | 0 | 
Air Cleaner ASM | 8981235322 | Cleaner ASM; air | Do not headline unless required by VIN | 0.3 | 2 | 
Air Cleaner ASM | 8982157230 | Cleaner ASM; air; used on some NPR75 rows | Do not headline unless required by VIN | 0.1 | 1 | 
Air Filter | 8981772710 | Filter; ACL | High campaign priority | 115.3 | 810 | 
Air Filter BVP | 5876102500 | BVP alternative for 8981772710 | Strong campaign item | 0.0 | 0 | 
Brake Pad Kit | 8982447940 | Pad kit; front/rear caliper application in matrix | Highest N75 focus item | 199.2 | 1,463 | 
Clutch Disc | 8981649171 | Manual only | Do not headline | 4.5 | 31 | 
Clutch Disc BVP | 5876100920 | BVP alternative for 8981649171 | Only if targeting manual units | 0.0 | 0 | 
Clutch Pressure Plate | 8970388314 | Manual only | Do not headline | 1.5 | 11 | 
Clutch Pressure Plate BVP | 5876101040 | BVP alternative for 8970388314 | Only if targeting manual units | 0.7 | 4 | 

## Slide 16: PMS Parts Promotion – NPR88 N75 4JZ1
PMS category | Part Number | Description / note | Campaign priority | Monthly Average | Year To Date Demand | Comments
Oil Filter | 8975439050 | Element kit; oil filter | High | 123.8 | 920 | 
Fuel Filter ASM | 8983104491 | Filter ASM; fuel | Medium-high | 1.0 | 5 | 
Fuel Filter ASM related | 8983104490 | Same HOF family reference | Use by VIN / supersession check | 0.0 | 0 | S/S TO 8983104491
Fuel Sedimenter | 8983572930 | Sedimenter; fuel | Medium | 0.3 | 1 | 
Fuel Filter Element | 8975425390 | Element kit; fuel filter | High | 148.6 | 1,090 | 
Fuel Filter Element | 8983752250 | Element kit; fuel filter | High | 1.2 | 7 | S/S TO 8975425390
Fuel Cartridge Kit | 8980374810 | Cartridge kit; fuel filter | High | 103.2 | 726 | 
Fuel Cartridge BVP | 5876101570 | BVP alternative for 8980374810 | Useful for price-sensitive customers | 65.7 | 499 | 
Fuel Cartridge related | 8980318470 | Related genuine reference under 8980374810 HOF | Use by VIN / supersession check | 0.0 | 0 | S/S TO 8980374810
Fuel Cartridge related | 8980179710 | Related genuine reference under 8980374810 HOF | Use by VIN / supersession check | 0.0 | 0 | S/S TO 8980374810
Air Cleaner ASM | 8976659910 | Cleaner ASM; air | Do not headline unless required by VIN | 0.1 | 0 | 
Air Filter | 8976739570 | Filter; ACL | High campaign priority | 70.8 | 474 | 
Brake Pad Kit | 8982447940 | Main NPR88 brake pad kit for most rows | Highest N75 focus item | 199.2 | 1,463 | 
Brake Pad Kit | 8982169220 | Used on specific NPR88 model-code groups | Secondary, VIN-specific | 53.0 | 359 | 
Brake Pad BVP | 5876102380 | BVP alternative for 8982169220 | Useful | 0.0 | 0 | 
Brake Pad BVP related | 5876170050 | Related BVP reference for 8982169220 family | Useful | 0.0 | 0 | 
Clutch Disc | 8978283700 | Manual only, some NPR88 rows | Do not headline | 0.3 | 1 | 
Clutch Disc | 8982551391 | Manual only, some NPR88 rows | Do not headline | 4.0 | 36 | 
Clutch Disc BVP | 5876100771 | BVP alternative for 8982551391 | Only if targeting manual units | 4.3 | 29 | 
Clutch Pressure Plate | 8980400932 | Manual only | Do not headline | 4.6 | 43 | 
Clutch Pressure Plate BVP | 5876100910 | BVP alternative for 8980400932 | Only if targeting manual units | 4.0 | 28 | 

## Slide 17: PMS Parts Promotion – NLR87 N35.125 RZ4E
PMS category | Part Number | Description / note | Campaign priority | Monthly Average | Year To Date Demand | Comments
Oil Filter | 8982705240 | Element; oil filter | High | 455.1 | 3,095 | 
Oil Filter BVP | 5876150530 | BVP alternative for 8982705240 | Useful for price-sensitive customers | 9.0 | 91 | 
Fuel Filter | 8975080920 | Filter ASM; fuel | High | 4.1 | 29 | 
Fuel Filter | 8975080932 | Filter ASM; fuel | High | 0.8 | 6 | 
Fuel Filter Element | 8981596930 | Element kit; fuel filter | High | 388.9 | 2,794 | 
Fuel Filter BVP | 5876150170 | BVP alternative for 8981596930 | Useful for price-sensitive customers | 20.8 | 127 | 
Fuel Filter Element | 8981941190 | Element kit; fuel filter | High | 407.4 | 2,787 | 
Fuel Filter BVP | 5876150240 | BVP alternative for 8981941190 | Useful for price-sensitive customers | 22.7 | 142 | 
Air Filter | 8983214130 | Filter; ACL | Highest N35 focus item | 83.5 | 641 | 
Air Filter BVP | 5876102900 | BVP alternative for 8983214130 | Strong campaign item | 25.9 | 187 | 
Air Cleaner ASM | 8975095290 | Cleaner ASM; air | Do not headline unless required by VIN | 0.6 | 6 | 
Front Brake Pad Kit | 8982169210 | Pad kit; caliper disc brake front | Brake inspection conversion | 66.7 | 497 | 
Front Brake Pad Kit | 8982169220 | Pad kit; caliper disc brake front | Brake inspection conversion | 53.0 | 359 | 
Brake Pad BVP | 5876102380 | BVP alternative for 8982169220 | Useful for price-sensitive repair channel | 0.0 | 0 | 
Rear Brake Shoe ASM | 8973319320 | Shoe ASM; rear brake | Secondary | 6.0 | 24 | 
Rear Brake Shoe Kit | 5878320440 | Shoe kit; rear brake | Secondary | 1.1 | 7 | 
Clutch Disc | 8983753331 | Manual only | Do not headline | 0.9 | 6 | 
Clutch Pressure Plate | 8982831940 | Manual only | Do not headline | 9.3 | 76 | 

## Slide 18: PMS Parts Promotion – NLR88 N35.150 4JZ1
PMS category | Main part number | Description / note | Campaign priority | Monthly Average | Year To Date Demand | Comments
Oil Filter | 8975439050 | Element kit; oil filter | Medium | 123.8 | 920 | 
Fuel Filter | 8983104491 | Filter ASM; fuel | Medium | 1.0 | 5 | 
Fuel Filter | 8977903031 | Filter ASM; fuel | Medium | 0.2 | 1 | 
Fuel Filter Element | 8981941190 | Element kit; fuel filter | Medium | 407.4 | 2,787 | 
Fuel Filter BVP | 5876150240 | BVP alternative for 8981941190 | Useful | 22.7 | 142 | 
Fuel Filter Element | 8975425390 | Element kit; fuel filter | High | 148.6 | 1,090 | 
Fuel Filter Element | 8983752250 | Element kit; fuel filter | High | 1.2 | 7 | S/S TO 8975425390
Air Filter | 8976739570 | Filter; ACL | Main NLR88 air-filter item | 70.8 | 474 | 
Air Cleaner ASM | 8976643531 | Cleaner ASM; air | Do not headline unless required by VIN | 0.1 | 0 | 
Front Brake Pad Kit | 8982169220 | Pad kit; caliper disc brake front | Brake inspection conversion | 53.0 | 359 | 
Rear Brake Pad Kit | 8982169210 | Pad kit; caliper rear | Brake inspection conversion | 66.7 | 497 | 
Brake Pad BVP | 5876102380 | BVP alternative for 8982169220 | Useful | 0.0 | 0 | 
Clutch Disc | 8978293170 | Manual only | Do not headline | 2.3 | 18 | 
Clutch Pressure Plate | 8980400932 | Manual only | Do not headline | 4.6 | 43 | 
Clutch Pressure Plate BVP | 5876100910 | BVP alternative for 8980400932 | Only if doing clutch targeting | 4.0 | 28 | 

## Slide 19: Support
1
SPA
2
Dealer Incentive